 UFR Series NFC reader API (Application Programming Interface)
uFR series of readers operates with Mifare® Classic and other RFID contactless cards and tags which communication interface is compliant to ISO / IEC 14443 standard, including NFC tags.
Since contactless RFID cards have a lot of specifics that are not supported by any standard Windows or other platform specific API, uFR Series readers are supplied with separate API interface placed in the dynamic library called uFCoder. Depending on platform and architecture, there are prefixes and suffixes to this name and also file extension.
Standard library package contains libraries for Windows x86 and x64 architecture (DLL's), Linux x86 and x64 (.so files), ARM and ARM HF (.so files), Mac OSX (.dylib files), header file (.h) and libraries for static linking ( .a and .lib files).
Alternatively this reader can communicate over a virtual COM port using appropriate available VCOM protocol. In this way, uFR Series readers can be used on any platform for which there is still no direct software support but there is existance of serial interface.
API specification (applies also to the VCOM protocol) contains functions that:
● emulate linear address space on the MIFARE® cards,
● directly addressing blocks on the MIFARE® card - the block address mode,
● indirectly addressing blocks on the MIFARE® cards, combining sector and blocks addresses within the sector - the sector address mode.
This way of data addressing is performed in accordance with the manufacturer's documentation for addressing the MIFARE® card.
Allows four methods of authentication for card data access:
● “Reader key authentication” - the default authentication mode. For this mode the keys are stored into the reader (with a maximum of 32 key with indexes from 0 to 31) and the key index is sent with related functions. In the case of functions that emulate linear address space in this method of authentication, the use of the same key for all sectors  (or at least for those who are in default range for linear addressing) is default.
● “Automatic key mode 1” (AKM1) and “Automatic key mode 2” (AKM2) are optional, automatic modes of authentication. This modes enable automatic selection of keys stored in the reader on the basis of the block address or a combination of block and sector address within the sector. These modes could be used in emulation of a linear address space because after the address conversion in the readers software it is performed automatic keys selection for the authentication of a block or sector. The difference between AKM1 and AKM2 is only in the way of automatic selection of A and B keys performing.
When using AKM1 mode it is accepted that the index keys in the reader from 0 to 15 are appropriate with A sectors keys from 0 to 15 and  the index keys in the reader from 16 to 31 are appropriate with  B sectors keys from 0 to 15.
When used AKM2 mode, even key indexes in the reader (0, 2, ..., 28, 30) are accepted as a sectors keys from 0 to 15 respectively and the odd key indexes in the reader are accepted as B sectors keys from 0 to 15. This is certainly true for Mifare ® 1K.
For MIFARE ® card MINI only the first five keys A and B can be used (in AKM1 key index from 0 to 4 for A keys and from 16 to 20 for B keys, in AKM2 mode for A key index 0, 2, 4, 6 and 8 and for B keys 1, 3, 5, 7 and 9) because this cards contain only that much sectors.
On MIFARE® 4K there are 40 sectors so the lower and upper address space are organized into the 2K. With these cards AKM1 and AKM2 modes are organized in such a way that the same keys  indexes from the reader corresponding sectors 0 to 15 and 16 to 32. For the last 8 sectors (sectors 32 to 39) the same readers keys are used that correspond to sectors 0 to 7 and 16 to 23.

The last method of authentication is "Provided key" (PK). In this mode, you do not use keys stored in the reader but the keys are sent directly from the code with API functions. This mode does not provide any security, so its use is not recommended except under strictly controlled conditions or for testing purposes.
A special function for the sector trailer blocks card entry is implemented which is a very simplified  calculation of the bytes values containing the access bits. This avoids the danger of permanently blocking the entire sectors of the card due to wrong bits format which controls access to blocks of a sector.
For those with more experience in working with MIFARE cards, the so-called unsafe option is left for the sector trailer blocks manipulation.
● There is a method for linear emulation mode, which formats the card sector trailer blocks in the same way ie. sets a unique keys and access bits for the entire card. This is a very simplified way of the card initialization for linear approach.
● API contains a set of functions for manipulating the cards value blocks.  Four-byte values read and write are supported with a value blocks automatically formatted for the appropriate specification. The increment and decrement blocks value is also supported.
General functions for working with the reader

ReaderOpen: Opens a port of connected reader. In the case of multi-thread applications, developers must be careful to synchronize access to readers resources to avoid unforeseen situations.
GetReaderType: Returns the device type identifier. On uFR readers this value is 0xD1150021.
GetReaderSerialNumber: Returns the device serial number.
ReaderSoftRestart: Reader is restarted by software. This function sets all readers operating parameters to the default values and resets the close RF field, which practically resets all the cards in the field.
ReaderReset: Resets all the digital logic of readers hardware. This function can generally caled in the event that ReaderSoftRestart did not gave the desired results.
ReaderClose: Closes readers port. This enables access to the reader from other processes.
ReaderStillConnected: This function checks if the reader is still connected on system.
    Functions declaration (C language):
  - UFR_STATUS ReaderStillConnected(unsigned int *connected);
  - connected – Pointer to "unsigned int" type variable 32 bit long, where the information about availability of the reader is written. If the reader is connected on system and fully functioning than function store 1 (true) in that variable, otherwise, on some error – store zero.
ReaderKeyWrite: Sets the keys for authentication to the reader when reading and manipulating data on the cards. The keys are entered in a special readers area in EEPROM that can not be read anymore which provided protection against unauthorized access.
Function declaration (C language):
unsigned long ReaderKeyWrite(const unsigned char *aucKey,
unsigned char ucKeyIndex);
- aucKey Pointer to an array of 6 bytes containing the key. Key bytes can have any value in the range 0 to 255. The transport keys on the new cards should have all the bits degrades gracefully (all key bytes have a value of 255)
- ucKeyIndex Index in the reader where the user intends to store the new key. Possible values ​​are 0 to 31.
ReaderUISignal: The function is used to control the reader light and sound signal. There are four modes of light signals and five sound modes.
Function declaration (C language):
unsigned long ReaderUISignal(unsigned char ucLightSignalMode,
        unsigned char ucBeepSignalMode);
- ucLightSignalMode Defines the light signals mode. It can have values from ​​0 to 4. A value of 0 indicates light signals inactivity.
- ucBeepSignalMode Defines the sound signals mode. It can have values from ​​0 to 5. A value of 0 indicates sound signals inactivity.
Functions for working with cards

By type of data they work with, the functions are classified in:
- Functions for manipulating card data blocks
- Functions for manipulating card value blocks.
According to the card data addressing method, this function are divided into:
- Functions that emulate the linear address space
- Functions that use bloc addressing
- Functions that use sector addressing
Functions for cards data manipulating are sorted according to the authentication method into the function sets recognizable by the suffix of the authentication method:
- “Reader key authentication” is the default authentication method so function of this group do not have any suffix
- Functions with the _AKM1 suffix use “Automatic key mode 1”
- Functions with the _AKM2 suffix use  “Automatic key mode 2”
Functions with the _PK suffix use “Provided key” method.

General functions for working with cards
GetCardId: This function returns the type identifier and card serial number placed into the reader. Reader supports only cards that have 4 byte serial number (UID size: single) according to the standard ISO / IEC 14443 A.
Functions that emulate the linear address space

- LinearRead
- LinearRead_AKM1
- LinearRead_AKM2
- LinearRead_PK
  Functions declaration (C language):
  unsigned long LinearRead(unsigned char *aucData,
          unsigned short usLinearAddress,
          unsigned short usDataLength,
          unsigned short *lpusBytesReturned,
          unsigned char ucAuthMode,
          unsigned char ucReaderKeyIndex);
  unsigned long LinearRead_AKM1(unsigned char *aucData,
          unsigned short usLinearAddress,
          unsigned short usDataLength,
          unsigned short *lpusBytesReturned,
          unsigned char ucAuthMode);
unsigned long LinearRead_AKM2(unsigned char *aucData,
        unsigned short usLinearAddress,
        unsigned short usDataLength,
        unsigned short *lpusBytesReturned,
        unsigned char ucAuthMode);
  unsigned long LinearRead_PK(unsigned char *aucData,
          unsigned short usLinearAddress,
          unsigned short usDataLength,
          unsigned short *lpusBytesReturned,
          unsigned char ucAuthMode,
          unsigned char *aucProvidedKey);
These functions are used for card data reading by using the linear address space emulation. The method for proving authenticity is determined by the suffix in the functions names:
- aucData - Pointer to the sequence of bytes where read data will be stored.
- usLinearAddress - Linear address on the card from which  the data want to read
- usDataLength - Number of bytes for reading. For aucData a minimum usDataLength bytes must be allocated before calling the function
- lpusBytesReturned - Pointer to "unsigned short" type variable, where the number of successfully read bytes from the card is written. If the reading is fully managed this data is equal to the usDataLength parameter. If there is an error reading some of the blocks, the function returns all successfully read data  in the aucData before the errors occurrence and the number of successfully read bytes is returned via this parameter
- ucAuthMode - This parameter defines whether to perform authentication with key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61).
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode, this applies to all sectors that are read
- aucProvidedKey - Pointer to the six-byte string containing the key for authenticity proving in the "Provided Key" method.  _PK Suffix in the name of the function indicates this method usage.

- LinearWrite,
- LinearWrite_AKM1,
- LinearWrite_AKM2,
- LinearWrite_PK
Functions declaration (C language):
unsigned long LinearWrite(const unsigned char *aucData,
        unsigned short usLinearAddress,
        unsigned short usDataLength,
        unsigned short *lpusBytesWritten,
        unsigned char ucAuthMode,
        unsigned char ucReaderKeyIndex);
unsigned long LinearWrite_AKM1(const unsigned char *aucData,
        unsigned short usLinearAddress,
        unsigned short usDataLength,
        unsigned short *lpusBytesWritten,
        unsigned char ucAuthKey);
unsigned long LinearWrite_AKM2(const unsigned char *aucData,
        unsigned short usLinearAddress,
        unsigned short usDataLength,
        unsigned short *lpusBytesWritten,
        unsigned char ucAuthKey);
unsigned long LinearWrite_PK(const unsigned char *aucData,
        unsigned short usLinearAddress,
        unsigned short usDataLength,
        unsigned short *lpusBytesWritten,
        unsigned char ucAuthKey,
        unsigned char *aucProvidedKey);
These functions are for writing data to the card using the emulation of linear address space. The method for proving authenticity is determined by the suffix in the functions names:
- aucData - Pointer to the sequence of bytes containing data for writing on the card
- usLinearAddress - Linear address of the card where the data writing is intend
- usDataLength - - Number of bytes for the entry. In aucData a minimum usDataLength bytes must be allocated before calling the function
- lpusBytesWritten - Pointer to a "unsigned short" type variable, where the number of successfully read bytes from the card is written. If the entry is a successfully completed this data is equal to the usDataLength parameter. If there was an error in writing some of the blocks, the function returns the number of successfully written bytes over this parameter
- ucAuthKey - This parameter defines whether to perform authentication with A key or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61)
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode, this applies to all sectors that are written
- aucProvidedKey - Pointer to the sixth byte string containing the key for authenticity proving in the "Provided Key" method.  _PK Suffix in the name of the function indicates this method usage.

- LinearFormatCard,
- LinearFormatCard_AKM1,
- LinearFormatCard_AKM2,
- LinearFormatCard_PK
Functions description:
These functions are used for  new keys A and B writing as well as access bits in the trailers of all card sectors. The setting of ninth trailers bytes is enabled (a general-purpose byte where any value can be entered). In all the card sector trailers the same value is set for the entire card so the same keys and access rights are valid. As it is necessary to prove the authenticity on the base of previous keys before writing into the sector trailers, these functions are potentially suitable to initialize the new card (the authentication is performed with transportation keys, all the key bytes are 0xFF) or to re-initialize the card with the same keys and access rights for all sectors. Certainly, there must always be careful about the previously set access rights (access bits) on the cards in case the changing of some keys or bits for access rights control is disabled.
Function declaration (C language):
unsigned long LinearFormatCard(const unsigned char *aucNewKeyA,
        unsigned char ucBlocksAccessBits,
        unsigned char ucSectorTrailersAccessBits,
        unsigned char ucSectorTrailersByte9,
        const unsigned char *aucNewKeyB,
        unsigned char *lpucSectorsFormatted,
        unsigned char ucAuthMode,
        unsigned char ucReaderKeyIndex);
unsigned long
LinearFormatCard_AKM1(const unsigned char *aucNewKeyA,
        unsigned char ucBlocksAccessBits,
        unsigned char ucSectorTrailersAccessBits,
        unsigned char ucSectorTrailersByte9,
        const unsigned char *aucNewKeyB,
        unsigned char *lpucSectorsFormatted,
        unsigned char ucAuthMode);
unaigned long
LinearFormatCard_AKM2(const unsigned char *aucNewKeyA,
        unsigned char ucBlocksAccessBits,
        unsigned char ucSectorTrailersAccessBits,
        unsigned char ucSectorTrailersByte9,
        const unsigned char *aucNewKeyB,
        unsigned char *lpucSectorsFormatted,
        unsigned char ucAuthMode);
unsigned long
LinearFormatCard(const unsigned char *aucNewKeyA,
        unsigned char ucBlocksAccessBits,
        unsigned char ucSectorTrailersAccessBits,
        unsigned char ucSectorTrailersByte9,
        const unsigned char *aucNewKeyB,
        unsigned char *lpucSectorsFormatted,
        unsigned char ucAuthMode,
        unsigned char *aucProvidedKey);
Greater flexibility in sector trailers initiating is offered by SectorTrailerWrite functions group :
- aucNewKeyA - Pointer on 6 bytes array containing a new A key
- ucBlocksAccessBits - The access bits values that define permissions for all data blocks on the card. It can have values ​​0 to 7
- ucSectorTrailersAccessBits - The access bits value that define access permissions for all the card sector trailers. It can have values ​​0 to 7
- ucSectorTrailersByte9 - The ninth byte value of all card sectors trailers. It can contain any value
- aucNewKeyB - Pointer on 6 bytes array containing a new B key
- lpucSectorsFormatted - Pointer to a "unsigned char" type variable through which the number of successfully formatted sectors trailers returns. Eg. if all the sectors trailers are successfully initialized, on the MIFARE® 1K, through this parameter it returns the value 16 which represents the number of sectors on this card. In case of error the parameter is an indication of the number of successfully initialized sectors starting from zero.
- ucAuthMode - This parameter defines whether to perform authentication A key or B key. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61).
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader.  In the linear address mode, this applies to all sectors that are written
aucProvidedKey - Pointer to the sixth byte string containing the key for authenticity proving in the "Provided Key" method.  _PK Suffix in the name of the function indicates this method usage.

Functions for working with data blocks
- BlockRead,
- BlockRead_AKM1,
- BlockRead_AKM2,
- BlockRead_PK,
Functions description:
This functions group is used for card block content reading. Always reads the entire block (16 bytes of the block). Functions use the so-called bloc addressing (the first card block has the address 0; first sector trailer has address 3, the next one 7, etc. until the last Mifare ® 1K block which is also a trailer of the last sector, has an address 63). These functions also allows reading of the sector trailers contents (its available part for reading, depending on the access rights set).
Functions declaration (C language):
unsigned long BlockRead(unsigned char *aucData,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode,
        unsigned char ucKeyIndex);
unsigned long BlockRead_AKM1(unsigned char *aucData,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode);
unsigned long BlockRead_AKM2(unsigned char *aucData,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode);
unsigned long BlockRead_PK(unsigned char *aucData,
        unsigned char block_address,
        unsigned char ucAuthMode,
        const unsigned char *aucProvidedKey);
- aucData - Pointer to the number of bytes where read data will be stored. Must be allocated  at least 16 bytes before calling the function.
- ucBlockAddress - ucAuthMode block address. This parameter defines whether to perform authentication A key or B key. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61).
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode, this applies to all sectors that are written
- aucProvidedKey - Pointer to the sixth byte array containing the key for authenticity proving in the "Provided Key" method.  _PK Suffix in the name of the function indicates this method usage.
These functions work the same as BlockRead group functions and are made for card block content reading. The only difference is that the sectoral addressing is used. That includes separately sending sector addresses and block addresses within a sector. For MIFARE® 1K card sector address may be in the range 0 to 15, and blocks address within the sector ranging from 0 to 3. For MIFARE ® 4k sector address may be in the range of 0 to 39 and since the second half of the address space organization is different (above 2 MB) blocks address in the last 8 sectors (sectors 32 to 39) may be in the range of 0 to 15. The entire block (16-byte block) is always read.
These functions can read the sector trailers contents (its available part for reading, depending on the  access rights set).
- aucData - Pointer to the bytes array where read data are going to be stored. At least 16 bytes must be allocated before the function is called
- ucSectorAddress - Sector Address
- ucBlockInSectorAddress - Block address within a sector
- ucAuthMode - This parameter defines whether to perform authentication with A key or B key. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61).
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode, this applies to all sectors that are written
- aucProvidedKey - Pointer to the sixth byte array containing the key for authenticity proving in the "Provided Key" method.  _PK Suffix in the name of the function indicates this method usage.
- BlockWrite,
- BlockWrite_AKM1,
- BlockWrite_AKM2,
- BlockWrite_PK
Functions description:
These functions are used for data entry (16 bytes at a time) into the card blocks. Functions use the so-called bloc addressing (the first card block has the address 0; first sector trailer has address 3, the next one 7, etc. until the last Mifare ® 1K block which is also a trailer of the last sector, has an address 63). This functions group don't allow direct data enter into the sector trailers. To do so, use the special functions SectorTrailerWrite and SectorTrailerWriteUnsafe.
Functions declaration (C language):
unsigned long BlockWrite(const unsigned char *aucData,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode,
        unsigned char ucKeyIndex);
unsigned long BlockWrite_AKM1(const unsigned char *aucData,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode);
unsigned long BlockWrite_AKM2(const unsigned char *aucData,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode);
unsigned long BlockWrite_PK(const unsigned char *aucData,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode,
        const unsigned char *aucProvidedKey);
- aucData - Pointer to the number of bytes where read data will be stored. Must be allocated  at least 16 bytes before calling the function
- ucBlockAddress - Cards block address
- ucAuthMode - This parameter defines whether to perform authentication with key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61).
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode, this applies to all sectors that are read
- aucProvidedKey - Pointer to the sixth byte array containing the key for authenticity proving in the "Provided Key" method.  _PK Suffix in the name of the function indicates this method usage.
FORBIDEN_DIRECT_WRITE_IN_SECTOR_TRAILER.
- BlockInSectorWrite,
- BlockInSectorWrite_AKM1,
- BlockInSectorWrite_AKM2,
- BlockInSectorWrite_PK
Function description:
These functions work the same as BlockWrite group functions,  they are used for data entry (16 bytes at a time) into card blocks. The only difference is the use of sector addressing. Sector addressing means separate sending sector and block addresses within a sector. For MIFARE® 1K card sector address may be in the range 0 to 15, and blocks address within the sector ranging from 0 to 3. For MIFARE ® 4k sector address may be in the range of 0 to 39 and since the second half of the address space organization is different (above 2 MB) blocks address in the last 8 sectors (sectors 32 to 39) may be in the range of 0 to 15. This functions group don't allow direct data enter into the sector trailers. To do so, use the special functions SectorTrailerWrite and SectorTrailerWriteUnsafe
Function declaration (C language)
unsigned long BlockWrite(const unsigned char *aucData,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        unsigned char ucKeyIndex);
unsigned long BlockWrite_AKM1(const unsigned char *aucData,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long BlockWrite_AKM2(const unsigned char *aucData,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long BlockWrite_PK(const unsigned char *aucData,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        const unsigned char *aucProvidedKey);
- aucData - Pointer to the number of bytes where read data will be stored. Must be allocated  at least 16 bytes before calling the function
- ucSectorAddress - Sector address
- ucBlockInSectorAddress - Block address in the sector
- ucAuthMode - This parameter defines whether to perform authentication with A key or B key. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61)
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode, this applies to all sectors that are written
- aucProvidedKey - Pointer to the sixth byte array containing the key for authenticity proving in the "Provided Key" method.  _PK Suffix in the name of the function indicates this method usage.
FORBIDEN_DIRECT_WRITE_IN_SECTOR_TRAILER.
- SectorTrailerWrite,
- SectorTrailerWrite_AKM1,
- SectorTrailerWrite_AKM2,
- SectorTrailerWrite_PK
Functions description:
These functions are used for data writing in the card sector trailers. Functions can also be used for sector trailers block addressing as well as for the sector addressing which is determined by the ucAddressingMode parameter. In the case of block addressing, the first card block has the address 0; trailer has a first sector address 3 and the next 7, etc. until the last block of Mifare® 1k which is also a trailer of the last sector and has an address 63. This group of functions simplifies the bits manipulation for blocks access rights setting (access bits) and minimizes the possibility of permanent blocking of the whole sector due to incorrect formatting of these bits. Formatting the access bits is made by the reader before the writing. API users can choose the appropriate blocks access rights which are represented by values ​​0 to 7 and to transmit them to these functions.

For sector trailers following access rights are valid:
- Access bits C1 C2 C3
- Access values (submitted to the function)
- Access rights
- Key A bytes containing the access bits and the nine byte key B
- Reading and writing

*) If the access rights for the sector trailer of an appropriate sector set up so that it is possible to readB Key, it can not be used for authentication in any of the cases. These functions also sets new sector keys if it is permitted to access rights.
For blocks the fallowing access rights are valid:
- Access bits C1 C2 C3
- Access values (submitted to the function)
- Access rights
- Reading, writing, increment, decrement
Functions declaration (C language):
unsigned long
SectorTrailerWrite(unsigned char ucAddressingMode,
        unsigned char ucAddress,
        const unsigned char *aucNewKeyA,
        unsigned char ucBlock0AccessBits,
        unsigned char ucBlock1AccessBits,
        unsigned char ucBlock2AccessBits,
        unsigned char ucSectorTrailerAccessBits,
        unsigned char ucSectorTrailerByte9,
        const unsigned char *aucNewKeyB,
        unsigned char ucAauthMode,
        unsigned char ucKeyIndex);
unsigned long
SectorTrailerWrite_AKM1(unsigned char ucAddressingMode,
        unsigned char ucAddress,
        const unsigned char *aucNewKeyA,
        unsigned char ucBlock0AccessBits,
        unsigned char ucBlock1AccessBits,
        unsigned char ucBlock2AccessBits,
        unsigned char ucSectorTrailerAccessBits,
        unsigned char ucSectorTrailerByte9,
        const unsigned char *aucNewKeyB,
        unsigned char ucAauthMode);
unsigned long
SectorTrailerWrite_AKM2(unsigned char ucAddressingMode,
        unsigned char ucAddress,
        const unsigned char *aucNewKeyA,
        unsigned char ucBlock0AccessBits,
        unsigned char ucBlock1AccessBits,
        unsigned char ucBlock2AccessBits,
        unsigned char ucSectorTrailerAccessBits,
        unsigned char ucSectorTrailerByte9,
        const unsigned char *aucNewKeyB,
        unsigned char ucAauthMode);
unsigned long
SectorTrailerWrite_PK(unsigned char ucAddressingMode,
        unsigned char ucAddress,
        const unsigned char *aucNewKeyA,
        unsigned char ucBlock0AccessBits,
        unsigned char ucBlock1AccessBits,
        unsigned char ucBlock2AccessBits,
        unsigned char ucSectorTrailerAccessBits,
        unsigned char ucSectorTrailerByte9,
        const unsigned char *aucNewKeyB,
        unsigned char ucAauthMode,,
        const unsigned char *aucProvidedKey);
- ucAddressingMode - Specifies the address mode. Possible values ​​of this parameter are BLOCK_ADDRESS_MODE (0x00) or SECTOR_ADDRESS_MODE (0x01). If any other value is sent the function returns an error code WRONG_ADDRESS_MODE
- ucAddress - Sectors or sector trailers blocks address, depending on ucAddressingMode. When using a sector-address mode, then, for instance, the MIFARE Classic 1K card, the range can be from 0 to 15 (this card has 16 sectors). The same card type in the block addressing mode can use the values from ​​0 to 63 provided that an error occurs if the addressed block is not also the sector trailer.
- aucNewKeyA - Pointer to the 6 byte array that represents a new A key for a specified sector which will be set if that is previously allowed with the access rights
- aucNewKeyB - Pointer to the six-byte array that represents a new B key for a specified sector which will be set if that is previously allowed with the access rights
- ucBlock0AccessBits - Access value for the 0 block of a sector.
MIFARE ® 4k has a different organization for the last 8 sectors, the second half of the address space. Therefore, in these sectors the access rights are set as follows:
- access rights to the first 5 blocks - ucBlock1AccessBits Access value block for the first sector
- prava pristupa drugih 5 blokova - ucBlock2AccessBits Access value block for the first sector
- access rights to the last 5 blocks:
  - ucSectorTrailerAccessBits - Access value for a sector trailer
  - ucSectorTrailerByte9 - The ninth sector trailers byte is a byte for general purpose where any single-byte value can be entered
  - ucAuthMode - This parameter defines whether to perform authentication with key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61)
  - ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode, this applies to all sectors that are written
  - aucProvidedKey - Pointer to the sixth byte array containing the key for authenticity proving in the "Provided Key" method.  _PK Suffix in the name of the function indicates this method usage.

- SectorTrailerWriteUnsafe,
- SectorTrailerWriteUnsafe_AKM1,
- SectorTrailerWriteUnsafe_AKM2,
- SectorTrailerWriteUnsafe_PK
Functions description:
These functions have the same purpose as the function of the SectorTrailerWrite group with the difference in sending the "raw" sector trailers content and the errors are possible while formatting ​​access bits values for entering. These functions are intended for developers with experience in working with MIFARE cards. All rules mentioned for the SectorTrailerWrite group functions applies to these functions, except the option of the "raw" data for sector trailer entry.
Functions declaration (C language):
unsigned long
SectorTrailerWriteUnsafe(unsigned char ucAddressingMode,
        unsigned char ucAddress,
        const unsigned char *aucSectorTrailer,
        unsigned char ucAauthMode,
        unsigned char key_index);
unsigned long
SectorTrailerWriteUnsafe_AKM1(unsigned char ucAddressingMode,
        unsigned char ucAddress,
        const unsigned char *aucSectorTrailer,
        unsigned char ucAauthMode);
nsigned long
SectorTrailerWriteUnsafe_AKM2(unsigned char ucAddressingMode,
        unsigned char ucAddress,
        const unsigned char *aucSectorTrailer,
        unsigned char ucAauthMode);
unsigned long
SectorTrailerWriteUnsafe_PK(unsigned char ucAddressingMode,
        unsigned char ucAddress,
        const unsigned char *aucSectorTrailer,
        unsigned char ucAauthMode,
        const unsigned char *aucProvidedKey);
- ucAddressingMode - Specifies the address mode. Possible values ​​of this parameter are BLOCK_ADDRESS_MODE (0x00) or SECTOR_ADDRESS_MODE (0x01). If any other value is been sent the function returns an error code WRONG_ADDRESS_MODE.
- ucAddress - Sectors or sector trailers block address, depending on ucAddressingMode.
When using a sector address mode, then,in the case of MIFARE ® 1K card, the range can  be from 0 to 15 (this card has 16 sectors) and the same card type in block addressing mode can use the values ​​0 to 63 with the possible error if the addressed block isn't also the sector trailer.
- aucSectorTrailer - Pointer to 6 byte array that contains the "raw" data for the address sector trailer entry
- ucAuthMode - This parameter defines whether to perform authentication key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61)
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode, this applies to all sectors that are written
aucProvidedKey - Pointer to the sixth byte array containing the key for authenticity proving in the "Provided Key" method.  _PK Suffix in the name of the function indicates this method usage.

Functions for working with value blocks
Value blocks represents an optional MIFARE® card functionality. This is actually a mode in which the entire block of data on the card (16 bytes) represents one four-byte value. In this mode, you can add any data block on the card (except of course, block 0, the zero sector and sector trailer). The values ​​in the value blocks are formatted in a special way and ​​in addition to value records contains the one byte address value, which gives users the added ability to implement the backup system.
D-Logic card readers takes care of the proper value blocks formatting so the set of functions that handle only with four byte values are available to users. It should be mentioned that the use of value blocks makes sense if the access rights to desired block are set on values ​​1, 6 or 0 (the default in new cards) which allows their values increment and decrement​. First of all, value blocks must be initiated, value and associated address must be in compliance with the appropriate format of sixteen byte records. The best and easiest way for value blocks initialization is with a set of API functions ValueBlockWrite or ValueBlockInSectorWrite.
- ValueBlockRead,
- ValueBlockRead_AKM1,
- ValueBlockRead_AKM2,
- ValueBlockRead_PK
Functions description:
These functions are used to read the fourth byte value of value blocks. In addition they are returning the associated address stored in the value block. Functions used block addressing (the first card block has the address 0; first sector trailer has address 3, the next one 7, etc. until the last Mifare ® 1K block which is also a trailer of the last sector, has an address 63)
Function declaration (C language):
unsigned long ValueBlockRead(long *lValue,
        unsigned char *ucValueAddr,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode,
        unsigned char ucKeyIndex);
unsigned long ValueBlockRead_AKM1(long *lValue,
        unsigned char *ucValueAddr,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode);
unsigned long ValueBlockRead_AKM1(long *lValue,
        unsigned char *ucValueAddr,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode);
unsigned long ValueBlockRead_PK(long *lValue,
        unsigned char *ucValueAddr,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode,
        const unsigned char *key);
- lValue - Pointer to a variable of a type "long" over which the block value returns
- ucValueAddr - Pointer to a variable of unsigned char type is returned via the one byte address which gives the added ability for a backup system implementation
- ucBlockAddress - Block address
- ucAuthMode - This parameter defines whether to perform authentication key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61).
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode it applies to all sectors for writing
- aucProvidedKey - Pointer to the six-byte array that contains the key for authentication of the "Provided Key" method. _PK function name suffix indicates to the use of this method.
- ValueBlockInSectorRead,
- ValueBlockInSectorRead_AKM1,
- ValueBlockInSectorRead_AKM2,
- ValueBlockInSectorRead_PK
Functions description
These functions do the same as ValueBlockRead group functions  and are proper for reading 4 byte values of the value blocks. In addition they return the associated address stored in the value block. The only difference is the use of so-called sectoral addressing. Sectoral addressing means separately sending sector and block addresses within a sector. For MIFARE® 1K card sector address may be in the range 0 to 15, and blocks address within the sector ranging from 0 to 3. For MIFARE ® 4k sector address may be in the range of 0 to 39 and since the second half of the address space organization is different (above 2 MB) blocks address in the last 8 sectors (sectors 32 to 39) may be in the range of 0 to 15.
Function declaration (C language):
unsigned long ValueBlockInSectorRead(long *lValue,
        unsigned char *ucValueAddr,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        unsigned char ucKeyIndex);
unsigned long ValueBlockInSectorRead_AKM1(long *lValue,
        unsigned char *ucValueAddr,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long ValueBlockInSectorRead_AKM1(long *lValue,
        unsigned char *ucValueAddr,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long ValueBlockInSectorRead_PK(long *lValue,
        unsigned char *ucValueAddr,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        const unsigned char *aucProvidedKey);
- lValue - Pointer to a variable of a long type over which the value block returns
- ucValueAddr - Pointer to a variable of unsigned char type is returned via the one byte address which gives the added ability for a backup system implementation
- ucSectorAddress - Sector address
- ucBlockInSectorAddress - Block address in a sector
- ucAuthMode - This parameter defines whether to perform authentication key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61)
- ucReaderKeyIndex - e default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode it applies to all sectors for writing
- aucProvidedKey - Pointer to the six-byte array that contains the key for authentication of the "Provided Key" method. _PK function name suffix indicates to the use of this method.
- ValueBlockWrite,
- ValueBlockWrite_AKM1,
- ValueBlockWrite_AKM2,
- ValueBlockWrite_PK

Functions description:
These functions are used to initialize and write fourth byte  value blocks values ​​and store the associated address in the value block. Functions using the so-called block addressing (the first card block has the address 0; trailer has a first sector address 3 and the next 7, etc. until the last block of Mifare® 1k which is also a trailer of the last sector and has an address 63).

Function declaration (C language):
unsigned long ValueBlockWrite(long lValue,
        unsigned char ucValueAddr,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode,
        unsigned char ucKeyIndex);
unsigned long ValueBlockWrite_AKM1(long lValue,
        unsigned char ucValueAddr,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode);
unsigned long ValueBlockWrite_AKM2(long lValue,
        unsigned char ucValueAddr,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode);
unsigned long ValueBlockWrite_PK(long lValue,
        unsigned char ucValueAddr,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode,
        const unsigned char *aucProvidedKey);

- lValue - Value for the value block entry
- ucValueAddr - Value block associated address
- ucBlockAddress - Block address
- ucAuthMode - This parameter defines whether to perform authentication with A key or B key. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61).
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode, this applies to all sectors that are written
- aucProvidedKey - Pointer to the sixth byte array containing the key for authenticity proving in the "Provided Key" method.  _PK Suffix in the name of the function indicates this method usage.

- ValueBlockInSectorWrite,
- ValueBlockInSectorWrite_AKM1,
- ValueBlockInSectorWrite_AKM2,
- ValueBlockInSectorWrite_PK
Functions description:
These functions are similar to the ValueBlockWrite group functions. They use for entry, ​​value blocks 4 bytes values initialization. In addition, stores the associated address into the block value. The only difference is the sectoral addressing usage. Sectoral addressing means separately sending sector and block addresses within a sector. For MIFARE® 1K card sector address may be in the range 0 to 15, and blocks address within the sector ranging from 0 to 3. For MIFARE ® 4k sector address may be in the range of 0 to 39 and since the second half of the address space organization is different (above 2 MB) blocks address in the last 8 sectors (sectors 32 to 39) may be in the range of 0 to 15.

Functions declaration (C language):
unsigned long ValueBlockInSectorWrite(long lValue,
        unsigned char ucValueAddr,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        unsigned char ucKeyIndex);
unsigned long ValueBlockInSectorWrite_AKM1(long lValue,
        unsigned char ucValueAddr,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long ValueBlockInSectorWrite_AKM2(long lValue,
        unsigned char ucValueAddr,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long ValueBlockInSectorWrite_PK(long lValue,
        unsigned char ucValueAddr,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        const unsigned char *aucProvidedKey);
- lValue - Values for the value block entry
- ucValueAddr - Value block associated address
- ucSectorAddress - Sector address
- ucBlockInSectorAddress - Block address of a sector
- ucAuthMode - This parameter defines whether to perform authentication key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61)
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode it applies to all sectors for writing
- aucProvidedKey - Pointer to the six-byte array that contains the key for authentication of the "Provided Key" method. _PK function name suffix indicates to the use of this method.
- ValueBlockIncrement,
- ValueBlockIncrement_AKM1,
- ValueBlockIncrement_AKM2,
- ValueBlockIncrement_PK
Functions description:
This feature set is used to increment the value 4 byte value blocks. The value of value block increment is sent as a parameter of these functions. Functions use block addressing (the first card block has the address 0; first sector trailer has address 3, the next one 7, etc. until the last Mifare ® 1K block which is also a trailer of the last sector, has an address 63).

Funcution declaration (C language):
unsigned long
ValueBlockInSectorIncrement(long lIncrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        unsigned char ucKeyIndex);
unsigned long
ValueBlockInSectorIncrement_AKM1(long lIncrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long
ValueBlockInSectorIncrement_AKM2(long lIncrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long
ValueBlockInSectorIncrement_PK(long lIncrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        const unsigned char *aucProvidedKey);
- lIncrementValue - The value of value block increment
- ucBlockAddress - Block adress in a sector
- ucAuthMode - This parameter defines whether to perform authentication key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61)
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode it applies to all sectors for writing
- aucProvidedKey - Pointer to the six-byte array that contains the key for authentication of the "Provided Key" method. _PK function name suffix indicates to the use of this method.

- ValueBlockInSectorIncrement,
- ValueBlockInSectorIncrement_AKM1,
- ValueBlockInSectorIncrement_AKM2,
- ValueBlockInSectorIncrement_PK
Functions description:
These functions has the same purpose as ValueBlockIncrement group functions and are used for reading 4 byte values of the value blocks.  The value of value block increment is sent as a parameter of these functions. The only difference is the sectoral addressing usage. Sectoral addressing means separately sending sector and block addresses within a sector. For MIFARE® 1K card sector address may be in the range 0 to 15, and blocks address within the sector ranging from 0 to 3. For MIFARE ® 4k sector address may be in the range of 0 to 39 and since the second half of the address space organization is different (above 2 MB) blocks address in the last 8 sectors (sectors 32 to 39) may be in the range of 0 to 15.

Functions declaration (C language):
unsigned long
ValueBlockInSectorIncrement(long lIncrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        unsigned char ucKeyIndex);
unsigned long
ValueBlockInSectorIncrement_AKM1(long lIncrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long
ValueBlockInSectorIncrement_AKM2(long lIncrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long
ValueBlockInSectorIncrement_PK(long lIncrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        const unsigned char *aucProvidedKey);
- lIncrementValue - The value of value block increment
- ucSectorAddress - Sector address
- ucBlockInSectorAddress - Block address within a sector
- ucAuthMode - This parameter defines whether to perform authentication key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61)
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode it applies to all sectors for writing
- aucProvidedKey - Pointer to the six-byte array that contains the key for authentication of the "Provided Key" method. _PK function name suffix indicates to the use of this method.

- ValueBlockDecrement,
- ValueBlockDecrement_AKM1,
- ValueBlockDecrement_AKM2,
- ValueBlockDecrement_PK
Functions description:
This set of functions is used to decrement 4 byte value of value blocks. The value of the value block decrement is sent as a parameter of these functions. Functions use block addressing (the first card block has the address 0; first sector trailer has address 3, the next one 7, etc. until the last Mifare ® 1K block which is also a trailer of the last sector, has an address 63).
Functions declaration (C language):
unsigned long ValueBlockDecrement(long lDecrementValue,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode,
        unsigned char ucKeyIndex);
unsigned long ValueBlockDecrement_AKM1(long lDecrementValue,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode);
unsigned long ValueBlockDecrement_AKM2(long lDecrementValue,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode);
unsigned long ValueBlockDecrement_PK(long lDecrementValue,
        unsigned char ucBlockAddress,
        unsigned char ucAuthMode,
        const unsigned char *aucProvidedKey);
- lDecrementValue - The value of value block decrement
- ucBlockAddress - Block address within a sector
- ucAuthMode - This parameter defines whether to perform authentication key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61)
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode it applies to all sectors for writing
- aucProvidedKey - Pointer to the six-byte array that contains the key for authentication of the "Provided Key" method. _PK function name suffix indicates to the use of this method.

- ValueBlockInSectorDecrement,
- ValueBlockInSectorDecrement_AKM1,
- ValueBlockInSectorDecrement_AKM2,
- ValueBlockInSectorDecrement_PK
Functions description:
These functions work the same as ValueBlockDecrement group functions and are made for the value blocks 4 byte values decrement.  The value of the value block decrement is sent as a parameter to these functions. Only difference is the sectoral addressing usage. That includes separately sending sector addresses and block addresses within a sector. For MIFARE® 1K card sector address may be in the range 0 to 15, and blocks address within the sector ranging from 0 to 3. For MIFARE ® 4k sector address may be in the range of 0 to 39 and since the second half of the address space organization is different (above 2 MB) blocks address in the last 8 sectors (sectors 32 to 39) may be in the range of 0 to 15
Function declaration (C language):
unsigned long
ValueBlockInSectorDecrement(long lDecrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        unsigned char ucKeyIndex);
unsigned long
ValueBlockInSectorDecrement_AKM1(long lDecrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long
ValueBlockInSectorDecrement_AKM2(long lDecrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode);
unsigned long
ValueBlockInSectorDecrement_PK(long lDecrementValue,
        unsigned char ucSectorAddress,
        unsigned char ucBlockInSectorAddress,
        unsigned char ucAuthMode,
        const unsigned char *aucProvidedKey);
- lDecrementValue - The value of value block decrement
- ucSectorAddress - Sector address
- ucBlockInSectorAddress - Block address within a sector
- ucAuthMode - This parameter defines whether to perform authentication key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61)
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode it applies to all sectors for writing
aucProvidedKey - Pointer to the six-byte array that contains the key for authentication of the "Provided Key" method. _PK function name suffix indicates to the use of this method.

Additional general functions for working with the cards
GetDlogicCardType
Function description:
This is a function that return a value that corresponds to the type of the detected card. Values of the card type defined in the following list:

#define DL_MIFARE_ULTRALIGHT	0x01
#define DL_MIFARE_ULTRALIGHT_EV1_11	0x02
#define DL_MIFARE_ULTRALIGHT_EV1_21	0x03
#define DL_MIFARE_ULTRALIGHT_C	0x04
#define DL_NTAG_203	0x05
#define DL_NTAG_210	0x06
#define DL_NTAG_212	0x07
#define DL_NTAG_213	0x08
#define DL_NTAG_215	0x09
#define DL_NTAG_216	0x0A
#define DL_MIFARE_MINI	0x20
#define DL_MIFARE_CLASSIC_1K	0x21
#define DL_MIFARE_CLASSIC_4K	0x22
#define DL_MIFARE_PLUS_S_2K	0x23
#define DL_MIFARE_PLUS_S_4K	0x24
#define DL_MIFARE_PLUS_X_2K	0x25
#define DL_MIFARE_PLUS_X_4K	0x26
#define DL_MIFARE_DESFIRE	0x27
#define DL_MIFARE_DESFIRE_EV1_2K	0x28
#define DL_MIFARE_DESFIRE_EV1_4K	0x29
#define DL_MIFARE_DESFIRE_EV1_8K	0x2A
If the card type is not supported, function return the value zero.
#define TAG_UNKNOWN	0x00
Function declaration (C language):
unsigned long GetDlogicCardType(unsigned char *lpucCardType);
Parameter description:
lpucCardType	Pointer to the variable in which the value of the card type written.

GetCardIdEx
Function description:
Function writes the card serial number card in a byte array, and also gives the length of the serial number of the card. Length of the serial number can be 4 (UID size: single), 7 (UID size: double) or 10 (UID size: triple) bytes, so it is necessary to define an array of 10 bytes which will be used to enter the card serial number.
Function declaration (C language):
unsigned long GetCardIdEx(unsigned char *lpuSak,
unsigned char *aucUid,
unsigned char *lpucUidSize);
Parameters description:
- lpuSak	Pointer to the variable in which the SAK (Select Acknowledge) written.
- AucUid	Pointer to array of bytes in which the card UID (Unique Identifier) written.
- LpucUidSize	Pointer to variable for the card UID size.

- GetLastCardIdEx
- Function description:
- Function get UID information from the uFReader about the last detected card. Function writes the card serial number card in a byte array, and also gives the length of the serial number of the card. It is necessary to define an array of 10 bytes which will be used to enter the card serial number.
- Function declaration (C language):
- unsigned long GetLastCardIdEx(unsigned char *lpuSak,
  unsigned char *aucUid,
  unsigned char *lpucUidSize);
- Parameters description:
- lpuSak	Pointer to the variable in which the SAK (Select Acknowledge) written.
- AucUid	Pointer to array of bytes in which the card UID (Unique Identifier) written.
- LpucUidSize	Pointer to variable for the card UID size.

# Function for DLL version reading
GetDllVersion
Function description:
The function returns the number of type unsigned long (4 bytes). The meaning of bytes in this number are presented in the table below.

0	1	2	3
DLL Major Version	DLL Minor Version	DLL Build

Example:
Function returns the number 0x00080202.
DLL Major Version = 2
DLL Minor Version = 2
DLL Build = 8
Function declaration (C language):
unsigned long GetDllVersion(void);

## Functions that support NDEF records
get_ndef_record_count
Function description:
Function returns the number of NDEF messages that have been read from the card, and number of NDEF records, number of NDEF empty messages. Also, function returns array of bytes containing number of messages pairs. First byte of pair is message ordinal, and second byte is number of NDEF records in that message. Message ordinal starts from 1.
Function declaration (C language)
unsigned long get_ndef_record_count(
unsigned char *ndef_message_cnt,
unsigned char *ndef_record_cnt,
unsigned char *ndef_record_array,
unsigned char *empty_ndef_message_cnt);
Parameters description:
- ndef_message_cnt	pointer to the variable containing number of NDEF messages
- ndef_record_cnt	pointer to the variable containing number of NDEF records
- ndef_record_array	pointer to the array of bytes containing pairs (message ordinal – number of records)
- empty_ndef_message_cnt	pointer to the variable containing number of empty messages

## read_ndef_record
Function description:
Function returns TNF, type of record, ID and payload from the NDEF record. NDEF record shall be elected by the message ordinal and record ordinal in this message.
Function declaration (C language)
unsigned long read_ndef_record(unsigned char message_nr,
unsigned char record_nr,
unsigned char *tnf,
unsigned char *type_record,
unsigned char *type_length,
unsigned char *id,
unsigned char *id_length,
unsigned char *payload,
unsigned long *payload_length);
Parameters description:
- message_nr	NDEF message ordinal (starts form 1)
- record_nr	NDEF record ordinal (in message)
- tnf	pointer to the variable containing TNF of record
- type_record	pointer to array containing type of record
- type_length	pointer to the variable containing length of type of record string
- id	pointer to array containing ID of record
- id_length	pointer to the variable containing length of ID of record string
- payload	pointer to array containing payload of record
- payload_length	pointer to the variable containing length of payload

write_ndef_record
Function description:
Function adds a record to the end of message, if one or more records already exist in this message. If current message is empty, then this empty record will be replaced with the record. Parameters of function are: ordinal of message, TNF, type of record, ID, payload. Function also returns pointer to the variable which reported that the card formatted for NDEF using (card does not have a capability container, for example new Mifare Ultralight, or Mifare Classic card).
Function declaration (C language)
unsigned long write_ndef_record(
unsigned char message_nr,
unsigned char *tnf,
unsigned char *type_record,
unsigned char *type_length,
unsigned char *id,
unsigned char *id_length,
unsigned char *payload,
unsigned long *payload_length,
unsigned char *card_formated);
Parameters description:
- message_nr	NDEF message ordinal (starts form 1)
- tnf	pointer to the variable containing TNF of record
- type_record	pointer to array containing type of record
- type_length	pointer to the variable containing length of type of record string
- id	pointer to array containing ID of record
- id_length	pointer to the variable containing length of ID of record string
- payload	pointer to array containing payload of record
- payload_length	pointer to the variable containing length of payload
- card_formated	pointer to the variable which shows that the card formatted for NDEF using.

erase_last_ndef_record
Function description:
Function deletes the last record of selected message. If message contains one record, then it will be written empty message.
Function declaration (C language)
unsigned long erase_last_ndef_record(unsigned char message_nr);
Parameter description:
- message_nr	NDEF message ordinal (starts form 1)
- erase_all_ndef_records
Function description:
Function deletes all records of message, then writes empty message.
Function declaration (C language)
unsigned long erase_all_ndef_records(unsigned char message_nr);
Parameter description:
message_nr	NDEF message ordinal (starts form 1)

ndef_card_initialization
Function description:
Function prepares the card for NDEF using. Function writes Capability Container (CC) if necessary, and writes empty message. If card is MIFARE CLASSIC or MIFARE PLUS, then function writes MAD (MIFARE Application Directory), and default keys and access bits for NDEF using.
Function declaration (C language)
unsigned long ndef_card_initialization(void);
### ERROR CODES OF NDEF FUNCTIONS
UFR_WRONG_NDEF_CARD_FORMAT = 0x80
UFR_NDEF_MESSAGE_NOT_FOUND = 0x81
UFR_NDEF_UNSUPPORTED_CARD_TYPE = 0x82
UFR_NDEF_CARD_FORMAT_ERROR = 0x83
UFR_MAD_NOT_ENABLED = 0x84
UFR_MAD_VERSION_NOT_SUPPORTED = 0x85

## Functions for configuration of asynchronously card ID sending
When the card put on the reader, then the string which contains card ID shall be sent. String contains hexadecimal notation of card ID, after that is one mandatory suffix character. Before the card ID may be one prefix character placed.
When the card is removed, then shall be sent the prefix and suffix without card ID.
Example:
Card ID is 0xA103C256, prefix is 0x58 ('X'), suffix is 0x59 ('Y')
String is “XA103C256Y” when card put on reader, and “XY” when card removed.
SetAsyncCardIdSendConfig
Function description:
Function sets the parameters of card ID sending. Parameters are: prefix existing, prefix character, suffix character, and baud rate for card ID sending.
Function declaration (C language)
unsigned long SetAsyncCardIdSendConfig(
unsigned char send_enable,
unsigned char prefix_enable,
unsigned char prefix,
unsigned char suffix,
unsigned char send_removed_enable,
unsigned long async_baud_rate);
Parameters description:
- send_enable	sending enable flag (0 – disabled, 1 – enabled )
- prefix_enable	prefix existing flag (0 – prefix don't exist, 1 – prefix exist)
- prefix	prefix character
- suffix	suffix character
- send_removed_enable	flag(0 – disabled, 1 - enabled)
- async_baud_rate	baud rate value (e.g. 9600)
- GetAsyncCardIdSendConfig
Function description:
Function returns the parameters of card ID sending.
Function declaration (C language)
unsigned long GetAsyncCardIdSendConfig(
unsigned char *send_enable,
unsigned char *prefix_enable,
unsigned char *prefix,
unsigned char *suffix,
unsigned char *send_removed_enable,
unsigned long *async_baud_rate);
Parameters description:
- send_enable	pointer to the sending enable flag
- prefix_enable	pointer to the prefix existing flag
- prefix	pointer to the prefix variable
- suffix	pointer to the suffix variable
- send_removed_enable	pointer to the flag
- async_baud_rate	pointer to the baud rate variable.

## Functions that works with Real Time Clock (RTC)
RTC embedded in uFR Advance device only.
GetReaderTime
Function description:
Function returns 6 bytes array of unsigned char that represented current date and time into device's RTC.
- Byte 0 represent year (current year – 2000)
- Byte 1 represent month (1 – 12)
- Byte 2 represent day of the month (1 – 31)
- Byte 3 represent hour (0 – 23)
- Byte 4 represent minute (0 – 59)
- Byte 5 represent second (0 – 59)
Function declaration (C language)
unsigned long GetReaderTime(unsigned char *time);
Parameter description:
time is pointer to the array containing current date and time representation.

SetReaderTime
Function description:
Function sets the date and time into device's RTC. Function requires the 8 bytes password entry to set date and time. Date and time are represent into 6 bytes array in same way as in GetReaderTime function. Factory password is “11111111” (0x31, 0x31, 0x31, 0x31, 0x31, 0x31, 0x31, 0x31).

Function declaration (C language)
unsigned long SetReaderTime(
unsigned char *password,
unsigned char *time);
Parameters description:
- password	pointer to the 8 bytes array containing password
- time	pointer to the 6 bytes array containing date and time representation

ChangeReaderPassword
Function description:
Function changes password for set date and time. Function's parameters are old password and new password.
Function declaration (C language)
unsigned long ChangeReaderPassword(
unsigned char *old_password,
unsigned char *new_password);
Parameters description:
- old_password	pointer to the 8 bytes array containing current password
- new_password	pointer to the 8 bytes array containing new password

## Functions that works with EEPROM
EEPROM embedded in uFR Advance device only.
Range of user address is from 0 to 32750.
ReaderEepromRead
Function description:
Function returns array of data read from EEPROM. Maximal length of array is 128 bytes.
Function declaration (C language)
unsigned long ReaderEepromRead(
unsigned char *data,
unsigned long address,
unsigned long size);
Parameters description:
- data	pointer to array containing data from EEPROM
- address	address of first data
- size	length of array

ReaderEepromWrite
Function description:
Function writes array of data into EEPROM. Maximal length of array is 128 bytes. Function requires password which length is 8 bytes. Factory password is “11111111” (0x31, 0x31, 0x31, 0x31, 0x31, 0x31, 0x31, 0x31).
Function declaration (C language)
unsigned long ReaderEepromWrite(
unsigned char *data,
unsigned long address,
unsigned long size,
unsigned char *password);
Parameters description:
- data	pointer to array containing data
- address	address of first data
- size	length of array
- password	pointer to array containing password

## Functions that works with Mifare Desfire Card (AES encryption in reader)
AES encryption and decryption is performed in the reader. AES keys are stored into reader.
uFR_int_WriteAesKey
Function description:
Function writes AES key (16 bytes) into reader.
Function declaration (C language)
unsigned long uFR_int_WriteAesKey(
unsigned char aes_key_nr,
unsigned char *aes_key);
Parameters description:
- aes_key_nr	ordinal number of AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- uFR_int_GetDesfireUid
- uFR_int_GetDesfireUid_PK
Function description:
Mifare Desfire EV1 card can be configured to use Random ID numbers instead Unique ID numbers during anti-collision procedure. In this case card uses single anti-collision loop, and returns Random Number Tag 0x08 and 3 bytes Random Number (4 bytes Random ID). This function returns Unique ID of card, if the Random ID is used.
Function declaration (C language)
unsigned long uFR_int_GetDesfireUid(
unsigned char aes_key_nr,
unsigned long aid,
unsigned char aid_key_nr,
unsigned char *card_uid,
unsigned char *card_uid_len,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_GetDesfireUid_PK(
unsigned char *aes_key_ext,
unsigned long aid,
unsigned char aid_key_nr,
unsigned char *card_uid,
unsigned char *card_uid_len,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- aes_key_nr	ordinal number of AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- aid	ID of application that uses this key (3 bytes long, 0x000000 for card master key)
- aid_key_nr	key number into application (0 for card master key or application master key)
- data	pointer to array containing card UID
- data_len	pointer to card UID length variable
- card_status	pointer to card error variable
- exec_time	function's execution time
ufr_int_DesfireFreeMem
Function description:
Function returns the available bytes on the card.
Function declaration (C language)
unsigned long uFR_int_DesfireFreeMem(
unsigned long *free_mem_byte,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- free_mem_byte	pointer to free memory size variable
- card_status	pointer to card error variable
- exec_time	function's execution time

- uFR_int_DesfireFormatCard
- uFR_int_DesfireFormatCard_PK
Function description:
Function releases all allocated user memory on the card. All applications will be deleted, also all files within those applications will be deleted. Only the card master key, and card master key settings will not be deleted. This operation requires authentication with the card master key.
Function declaration (C language)
unsigned long uFR_int_DesfireFormatCard(
unsigned char aes_key_nr,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireFormatCard_PK(
unsigned char *aes_key_ext,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- aes_key_nr	ordinal number of card master AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- card_status	pointer to card error variable
- exec_time	function's execution time

- uFR_int_DesfireSetConfiguration
- uFR_int_DesfireSetConfiguration_PK
Function description:
Function allows you to activate the Random ID option, and/or Format disable option.
If these options are activated, then they can not be returned to the factory setting (Random ID disabled, Format card enabled). This operation requires authentication with the card master key.
Function declaration (C language)
unsigned long uFR_int_DesfireSetConfiguration(
unsigned char aes_key_nr,
unsigned char random_uid,
unsigned char format_disable,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireSetConfiguration_PK(
unsigned char *aes_key_ext,
unsigned char random_uid,
unsigned char format_disable,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- aes_key_nr	ordinal number of card master AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- random_uid	0 – Random ID disabled, 1 – Random ID enabled
- format_disable	0 – Format enabled, 1 – Format disabled
- card_status	pointer to card error variable
- exec_time	function's execution time

- uFR_int_DesfireGetKeySettings
- uFR_int_DesfireGetKeySettings_PK
Function description:
Function allows to get card master key and application master key configuration settings. In addition it returns the maximum number of keys which can be stored within selected application.
Function declaration (C language)
unsigned long uFR_int_DesfireGetKeySettings(
unsigned char aes_key_nr,
unsigned long aid,
unsigned char *settings
unsigned char *max_key_no,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireGetKeySettings_PK(
unsigned char *aes_key_ext,
unsigned long aid,
unsigned char *settings
unsigned char *max_key_no,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- aes_key_nr	ordinal number of AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- aid	ID of application that uses this key (3 bytes long, 0x000000 for card master key)
- settings	pointer to settings variable
- max_key_no	maximum number of keys within selected application
- card_status	pointer to card error variable
- exec_time	function's execution time

- uFR_int_DesfireChangeKeySettings
- uFR_int_DesfireChangeKeySettings_PK
Function description:
Function allows to set card master key, and application master key configuration settings.
Function declaration (C language)
unsigned long uFR_int_DesfireChangeKeySettings(
unsigned char aes_key_nr,
unsigned long aid,
unsigned char settings,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireChangeKeySettings_PK(
unsigned char *aes_key_ext,
unsigned long aid,
unsigned char settings,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- aes_key_nr	ordinal number of AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- aid	ID of application that uses this key (3 bytes long, 0x000000 for card master key)
- settings	pointer to key settings variable
- card_status	pointer to card error variable
- exec_time	function's execution time

- uFR_int_DesfireChangeAesKey
- uFR_int_DesfireChangeAesKey_PK
Function description:
Function allow to change any AES key on the card. Changing the card master key require current card master key authentication. Authentication for the application keys changing depend on the application master key settings (which key uses for authentication).
Function declaration (C language)
unsigned long uFR_int_DesfireChangeAesKey(
unsigned char aes_key_nr,
unsigned long aid,
unsigned char aid_key_nr_auth,
unsigned char new_aes_key[16],
unsigned char aid_key_no,
unsigned char old_aes_key[16],
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireChangeAesKey_PK(
unsigned char *aes_key_ext,
unsigned long aid,
unsigned char aid_key_nr_auth,
unsigned char new_aes_key[16],
unsigned char aid_key_no,
unsigned char old_aes_key[16],
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- aes_key_nr	ordinal number of AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- aid	ID of application that uses this key (3 bytes long, 0x000000 for card master key)
- aid_key_nr_auth	key number into application which uses for authentication
- new_aes_key[16]	16 bytes array that represent AES key
- aid_key_no	key number into application that will be changed
- old_aes_key[16]	16 bytes array that represent current AES key that will be changed, if this is not key by which is made authentication.
- card_status	pointer to card error variable
- exec_time	function's execution time

- uFR_int_DesfireCreateAesApplication
- uFR_int_DesfireCreateAesApplication_PK
- uFR_int_DesfireCreateAesApplication_no_auth
Function description:
Function allows to create new application on the card. Is the card master key authentication is required, depend on the card master key settings. Maximal number of applications on the card is 28. Each application is linked to set of up 14 different user definable access keys.
Function declaration (C language)
unsigned long uFR_int_DesfireCreateApplication(
unsigned char aes_key_nr,
unsigned long aid_nr,
unsigned char settings,
unsigned char max_key_no,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireCreateApplication_PK(
unsigned char *aes_key_ext,
unsigned long aid_nr,
unsigned char settings,
unsigned char max_key_no,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireCreateApplication_no_auth(
unsigned long aid_nr,
unsigned char settings,
unsigned char max_key_no,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- aes_key_nr	ordinal number of card master AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- aid_nr	ID of application that creates (3 bytes long 0x000000 to 0xFFFFFF)
- settings	application master key settings
- max_key_no	maximal number of keys into application
- card_status	pointer to card error variable
- exec_time	function's execution time
- uFR_int_DesfireDeleteApplication
- uFR_int_DesfireDeleteApplication_PK
Function description:
Function allows to deactivate application on the card. Is the card master key authentication is required, depend on the card master key settings. AID allocation is removed, but deleted memory blocks can only recovered by using Format card function.
Function declaration (C language)
unsigned long uFR_int_DesfireDeleteApplication(
unsigned char aes_key_nr,
unsigned long aid_nr,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireDeleteApplication_PK(
unsigned char *aes_key_ext,
unsigned long aid_nr,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- aes_key_nr	ordinal number of card master AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- aid_nr	ID of application that deletes (3 bytes long 0x000000 to 0xFFFFFF)
- card_status	pointer to card error variable
- exec_time	function's execution time

- uFR_int_DesfireCreateStdDataFile
- uFR_int_DesfireCreateStdDataFile_PK
- uFR_int_DesfireCreateStdDataFile_no_auth
Function description:
Function allows to create file for the storage unformatted user data within existing application on the card. Maximal number of files into application is 32. The file will be created in the currently selected application. Is the application master key authentication is required, depend on the application master key settings.
Communication settings define communication mode between reader and card. The communication modes are:
- plain communication	communication settings value is 0x00
- plain communication secured by MACing	communication settings value is 0x01
- fully enciphered communication	communication settings value is 0x11
Access rights for read, write, read&write and changing, references certain key within application's keys (0 – 13). If value is 14, this means free access, independent of previous authentication. If value is 15, this means deny access (for example if write access is 15 then the file type is read only).
Function declaration (C language)
unsigned long uFR_int_DesfireCreateStdDataFile(
unsigned char aes_key_nr,
unsigned long aid,
unsigned char file_id,
unsigned long file_size,
unsigned char read_key_no,
unsigned char write_key_no,
unsigned char read_write_key_no,
unsigned char change_key_no,
unsigned char communication_settings,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireCreateStdDataFile_PK(
unsigned char *aes_key_ext,
unsigned long aid,
unsigned char file_id,
unsigned long file_size,
unsigned char read_key_no,
unsigned char write_key_no,
unsigned char read_write_key_no,
unsigned char change_key_no,
unsigned char communication_settings,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireCreateStdDataFile_no_auth(
unsigned long aid,
unsigned char file_id,
unsigned long file_size,
unsigned char read_key_no,
unsigned char write_key_no,
unsigned char read_write_key_no,
unsigned char change_key_no,
unsigned char communication_settings,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- aes_key_nr	ordinal number of AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- aid	ID of application that contains the file
- file_id	ID of file that will be created (0 – 31)
- file_size	file size in bytes
- read_key_no	key for reading
- write_key_no	key for writing
- read&write_key_no	key for reading and writing
- change_key_no	key for changing this setting
- communication_settings	variable that contains communication settings
- card_status	pointer to card error variable
- exec_time	function's execution time

- uFR_int_DesfireDeleteFile
- uFR_int_DesfireDeleteFile_PK
- uFR_int_DesfireDeleteFile_no_auth
Function description:
Function deactivates a file within currently selected application. Allocated memory blocks associated with deleted file not set free. Only format card function can delete the memory blocks. Is the application master key authentication is required, depend on the application master key settings.
Function declaration (C language)
unsigned long uFR_int_DesfireDeleteFile(
unsigned char aes_key_nr,
unsigned long aid,
unsigned char file_id,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireDeleteFile_PK(
unsigned char *aes_key_ext,
unsigned long aid,
unsigned char file_id,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireDeleteFile_no_auth(
unsigned long aid,
unsigned char file_id,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- internal_key	1 - AES key stored into reader uses for authentication, 0 – AES key uses for authentication entered as a function's parameter
- aes_key_nr	ordinal number of AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- aid	ID of application that contains the file
- file_id	ID of file that will be deleted (0 – 31)
- auth_req	value is 1 if authentication is needed, otherwise it is 0
- card_status	pointer to card error variable
- exec_time	function's execution time

- uFR_int_DesfireReadStdDataFile
- uFR_int_DesfireReadStdDataFile_PK
- uFR_int_DesfireReadStdDataFile_no_auth
Function description:
Function allow to read data from Standard Data File, or from Backup Data File. Read command requires a preceding authentication either with the key specified for Read or Read&Write access.
Function declaration (C language)
unsigned long uFR_int_DesfireReadStdDataFile(
unsigned char aes_key_nr,
unsigned long aid,
unsigned char aid_key_nr,
unsigned char file_id,
unsigned short offset,
unsigned short data_length,
unsigned char communication_settings,
unsigned char *data,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireReadStdDataFile_PK(
unsigned char *aes_key_ext,
unsigned long aid,
unsigned char aid_key_nr,
unsigned char file_id,
unsigned short offset,
unsigned short data_length,
unsigned char communication_settings,
unsigned char *data,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireReadStdDataFile_no_auth(
unsigned long aid,
unsigned char aid_key_nr,
unsigned char file_id,
unsigned short offset,
unsigned short data_length,
unsigned char communication_settings,
unsigned char *data,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- aes_key_nr	ordinal number of AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- aid	ID of application that contains the file
- aid_key_nr	key number into application
- file_id	ID of file (0 – 31)
- offset	start position for read operation within file
- data_length	number of data to be read
- communication_settings	value must be same as in file declaration
- data	pointer to data array
- card_status	pointer to card error variable
- exec_time	function's execution time

- uFR_int_DesfireWriteStdDataFile
- uFR_int_DesfireWriteStdDataFile_PK
- uFR_int_DesfireWriteStdDataFile_no_auth
Function description:
Function allow to write data to Standard Data File, or to Backup Data File. Write command requires a preceding authentication either with the key specified for Write or Read&Write access.
Function declaration (C language)
unsigned long uFR_int_DesfireWriteStdDataFile(
unsigned char aes_key_nr,
unsigned long aid,
unsigned char aid_key_nr,
unsigned char file_id,
unsigned short offset,
unsigned short data_length,
unsigned char communication_settings,
unsigned char *data,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireWriteStdDataFile_PK(
unsigned char *aes_key_ext,
unsigned long aid,
unsigned char aid_key_nr,
unsigned char file_id,
unsigned short offset,
unsigned short data_length,
unsigned char communication_settings,
unsigned char *data,
unsigned short *card_status,
unsigned short *exec_time);
unsigned long uFR_int_DesfireWriteStdDataFile_no_auth(
unsigned long aid,
unsigned char aid_key_nr,
unsigned char file_id,
unsigned short offset,
unsigned short data_length,
unsigned char communication_settings,
unsigned char *data,
unsigned short *card_status,
unsigned short *exec_time);
Parameters description:
- aes_key_nr	ordinal number of AES key in the reader
- aes_key_ext	pointer to 16 byte array containing the AES key
- aid	ID of application that contains the file
- aid_key_nr	key number into application
- file_id	ID of file (0 – 31)
- offset	start position for write operation within file
- data_length	number of data to be written
- communication_settings	value must be same as in file declaration
- data	pointer to data array
- card_status	pointer to card error variable
- exec_time	function's execution time

DES_to_AES_key_type
Function description:
Function allow to change the card master key type from DES to AES. Factory setting for DESFIRE card master key is DES key type, and value is 0x0000000000000000. Because the reader uses AES keys, you must change the type key on AES. New AES key is 0x00000000000000000000000000000000.
Function declaration (C language)
unsigned long DES_to_AES_key_type(void);

## Functions for for the operating parameters of the reader setting
UfrSetBadSelectCardNrMax
Function description:
The function allows you to set the number of unsuccessful card selections before it can be considered that the card is not placed on the reader. Period between two card selections is approximately 10ms. Default value of this parameter is 20 i.e. 200ms. This parameter can be set in the range of 0 to 254.
This is useful for asynchronous card ID transmission, if parameter send_removed_enable in function SetAsyncCardIdSendConfig is set. Then you can set a lower value of the number of unsuccessful card selections, in order to send information to the card removed was faster.
A small value of this parameter may cause a false report that the card is not present, and immediately thereafter true report that the card is present.
Function declaration (C language)
unsigned long UfrSetBadSelectCardNrMax(
unsigned char bad_select_nr_max);
UfrGetBadSelectCardNrMax
Function description:
The function returns value of maximal unsuccessful card selections, which is set in reader.
Function declaration (C language)
unsigned long UfrGetBadSelectCardNrMax(
unsigned char *bad_select_nr_max);

## Functions for all blocks linear reading
Functions allow you to quickly read data from the card including the sector trailer blocks. These functions are very similar to the functions for linear reading of users data space.
- LinearRowRead
- LinearRowRead_AKM1
- LinearRowRead_AKM2
- LinearRowRead_PK
  Functions declaration (C language):
  unsigned long LinearRowRead(unsigned char *aucData,
          unsigned short usLinearAddress,
          unsigned short usDataLength,
          unsigned short *lpusBytesReturned,
          unsigned char ucAuthMode,
          unsigned char ucReaderKeyIndex);
  unsigned long LinearRowRead_AKM1(unsigned char *aucData,
          unsigned short usLinearAddress,
          unsigned short usDataLength,
          unsigned short *lpusBytesReturned,
          unsigned char ucAuthMode);
unsigned long LinearRowRead_AKM2(unsigned char *aucData,
        unsigned short usLinearAddress,
        unsigned short usDataLength,
        unsigned short *lpusBytesReturned,
        unsigned char ucAuthMode);
  unsigned long LinearRowRead_PK(unsigned char *aucData,
          unsigned short usLinearAddress,
          unsigned short usDataLength,
          unsigned short *lpusBytesReturned,
          unsigned char ucAuthMode,
          unsigned char *aucProvidedKey);
The method for proving authenticity is determined by the suffix in the functions names:
- aucData - Pointer to the sequence of bytes where read data will be stored.
- usLinearAddress - Linear address on the card from which  the data want to read
- usDataLength - Number of bytes for reading. For aucData a minimum usDataLength bytes must be allocated before calling the function
- lpusBytesReturned - Pointer to "unsigned short" type variable, where the number of successfully read bytes from the card is written. If the reading is fully managed this data is equal to the usDataLength parameter. If there is an error reading some of the blocks, the function returns all successfully read data  in the aucData before the errors occurrence and the number of successfully read bytes is returned via this parameter
- ucAuthMode - This parameter defines whether to perform authentication with key A or key B. It can have two values, namely: AUTHENT1A (0x60) or AUTHENT1B (0x61).
- ucReaderKeyIndex - The default method of authentication (when the functions without a suffix is used) performs the authenticity proving by using the selected key index from the reader. In the linear address mode, this applies to all sectors that are read
- aucProvidedKey - Pointer to the six-byte string containing the key for authenticity proving in the "Provided Key" method.  _PK Suffix in the name of the function indicates this method usage.

## FUNCTIONS FOR READER LOW POWER MODE CONTROL
UfrEnterSleepMode
Function allows enter to reader low power working mode. Reader is in sleep mode. RF field is turned off. The reader is waiting for the command to return to normal working mode.
Functions declaration (C language):
unsigned long UfrEnterSleepMode(void);

UfrLeaveSleepMode
Function allows return from low power reader mode to normal working mode.
Functions declaration (C language):
unsigned long UfrLeaveSleepMode(void);

### AutoSleepSet from firmware version 3.8.18 and lib version 3.8.15
This function permanently set auto-sleep functionality of the device. Valid seconds_wait range is from 1 to 254. To permanently disable auto-sleep functionality use 0 or 0xFF for the seconds_wait parameter.
Function declaration (C language):
unsigned long AutoSleepSet(uint8_t seconds_wait);
### AutoSleepGet from firmware version 3.8.18 and lib version 3.8.15
This function uses to get auto-sleep functionality setup from the device. You have to send pointer to already allocated variable of the uint8_t type. If auto-sleep functionality is disabled you will get 0 or 0xFF in the variable pointed by the *seconds_wait parameter.
Function declaration (C language):
unsigned long AutoSleepGet(uint8_t *seconds_wait);

## Functions for Reader NTAG Emulation Mode
### WriteEmulationNdef
Function description:
Function store a message record for NTAG emulation mode in to the reader. Parameters of the function are: TNF, type of record, ID, payload.
Function declaration (C language):
unsigned long WriteEmulationNdef(uint8_t tnf,
       uint8_t* type_record,
       uint8_t type_length,
       uint8_t* id,
       uint8_t id_length,
       uint8_t* payload,
       uint8_t payload_length);
Parameters description:
- tnf	TNF of the record
- type_record	pointer to the array containing record type
- type_length	length of the record type
- id	pointer to the array containing record ID
- id_length	length of the record ID
- payload	pointer to the array containing record payload
- payload_length	length of the record payload
Possible error codes:
WRITE_VERIFICATION_ERROR = 0x70
MAX_SIZE_EXCEEDED = 0x10

### TagEmulationStart
Put the reader permanently in a NDEF tag emulation mode. Only way for a reader to exit from this mode is to receive the TAG_EMULATION_STOP command (issued by calling TagEmulationStop() function).
In this mode, the reader can only answer to the commands issued by a following library functions:
TagEmulationStart(),
WriteEmulationNdef(),
TagEmulationStop(),
GetReaderSerialNumber(),
GetReaderSerialDescription(),
GetReaderHardwareVersion(),
GetReaderFirmwareVersion(),
GetBuildNumber()
Calls to the other functions in this mode returns following error code:
FORBIDDEN_IN_TAG_EMULATION_MODE = 0x90
Function declaration (C language):
unsigned long TagEmulationStart(void);
Possible error codes:
WRITE_VERIFICATION_ERROR = 0x70
(command resulting in a direct write to a device non-volatile memory)

### TagEmulationStop
Allows the reader permanent exit from a NDEF tag emulation mode.
Function declaration (C language):
unsigned long TagEmulationStop(void);
Possible error codes:
WRITE_VERIFICATION_ERROR = 0x70
(command resulting in a direct write to a device non-volatile memory)

## Functions for setting Reader baud rates for ISO14443 – 4A cards
### SetSpeedPermanently
Function declaration (C language):
unsigned long SetSpeedPermanently(uint8_t tx_speed, uint8_t rx_speed);
Parameters description:
- tx_speed – setup value for transmit speed
- rx_speed – setup value for receive speed
Valid speed setup values are:
Const	Configured speed
0	106 kbps (default)
1	212 kbps
2	424 kbps

On some reader types maximum rx_speed is 212 kbps. If you try to set higher speed than is allowed, reader firmware will automatically set the maximum possible speed.

Possible error codes:
WRITE_VERIFICATION_ERROR = 0x70
(command resulting in a direct write to a device non-volatile memory)

### GetSpeedParameters
Function declaration (C language):
unsigned long GetSpeedParameters(uint8_t* tx_speed, uint8_t* rx_speed);
Parameters description:
- tx_speed – returns configured value for transmit speed
- rx_speed – returns configured value for receive speed

## FUNCTIONS FOR DISPLAY CONTROL
SetDisplayData
Function enables sending data to the display. A string of data contains information about the intensity of color in each cell of the display. Each cell has three LED (red, green and blue). For each cell of the three bytes is necessary. The first byte indicates the intensity of the green color, the second byte indicates the intensity of the red color, and the third byte indicates the intensity of blue color. For example, if the display has 16 cells, an array contains 48 bytes. Value of intensity is in range from 0 to 255.
Function declaration (C language)
unsigned long SetDisplayData(unsigned char *display_data,	unsigned char data_length);
Parameters description.
- display_data – pointer to data array
- data_length – number of data into array

SetSpeakerFrequency
Function sets the frequency of the speaker. The speaker is working on this frequency until a new frequency setting. To stop the operation set frequency to zero.
Function declaration (C language)
unsigned long SetSpeakerFrequency(uint16_t frequency);
Parameters description
frequency – frequency in Hz
### FUNCTIONS TO USE THE SHARED RAM INTO DEVICE
Shared RAM is memory space on a device that is used for communication between computer and Android device (phone, tablet) with an NFC reader. PC writes and read data from shared RAM via USB port. Device with Android OS writes and read data from shared RAM via NFC.
EnterShareRamCommMode
Put reader permanently in the mode that use shared RAM. After execution of this function, must be executed function TagEmulationStart.
Function declaration (C language):
unsigned long EnterShareRamCommMode(void);

ExitShareRamCommMode
The permanent exit from mode that use shared RAM. After execution of this function, must be executed function TagEmulationStop.
Function declaration (C language):
unsigned long EnterShareRamCommMode(void);

WriteShareRam
Function allows writing data to the shared RAM.
Function declaration (C language):
unsigned long WriteShareRam(uint8_t *ram_data,
uint8_t addr,
uint8_t data_len);
Parameters description:
- ram_data – pointer to data array
- addr – address of first data in an array
- data_len – length of array. Address + data_len <= 184

ReadShareRam
Function allows read data from the shared RAM.
Function declaration (C language)
unsigned long ReadShareRam(uint8_t *ram_data,
uint8_t addr,
uint8_t data_len);